## Slide 1
EXECUTIVE SUMMARY
Two terminals.
One of them is live.
How we keep the analysis tuned to a moving market — without changing the numbers under people's feet.
Active / hot-standby terminal design · Approved in principle, 12 September 2026 · Not yet built
TERMINAL A
Live — this is what you see
TERMINAL B
Rehearsing — nobody is watching
they swap places
Notes: Executive summary of the active / hot-standby terminal design. Status: approved in principle on 12 Sep 2026, not yet built. Four beats: why we retune, what retuning costs today, the two-terminal fix, and the one catch that changes what gets built.

## Slide 2
THE WHOLE THING IN ONE MINUTE
Four steps, start to finish
1
Markets move
The settings behind our channel drawings are fitted to how the market has recently behaved. The market keeps moving, so those settings go stale. Someone has to retune them — continuously.
2
Today we retune live
Changing a setting on the live terminal rewrites about two weeks of past values in place. Nothing anywhere records that it happened, or what the numbers used to be.
3
The fix: a rehearsal room
Run a second terminal that nobody reads. Tune it there, check it by eye, then make it the live one with a single switch. The old one stays running as the undo.
4
The catch worth knowing
The folder those terminals hand over is read by four separate systems, not one. Switch carelessly and two unrelated features stop working — with no error anywhere.
The result: the same service, never offline — but change that is deliberate, checked before anyone sees it, and reversible.
Notes: The four-beat narrative. Beat 4 is the one that is not obvious from any existing diagram and is the reason the build is three terminals rather than two.

## Slide 3
STEP 1 — THE NEED
Why the settings keep going stale
Chart: 
Where the market actually went | 50 | 47 | 52 | 49 | 54 | 51 | 56 | 53 | 58 | 61 | 57 | 63 | 66 | 62 | 69 | 72 | 68 | 76
What the tuned setting still expects | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
The lines we draw on the chart are fitted to a window of recent market behaviour. As price moves on, that fit stops describing what is actually happening now.
Fitted to yesterday
The settings describe a market that has already passed.
Drifts a little further each week
Nothing breaks. It just gets steadily less right.
Only a human eye catches it
Nothing in the system raises a hand and says so.
So retuning is not an occasional repair. It is routine, ongoing work.
Notes: The need. Indicator configurations are fitted to a recent window and go stale as the market forms new structure. Retuning is continuous administrator work, not an occasional fix.

## Slide 4
STEP 2 — THE COST TODAY
What retuning costs us right now
You change a setting
On the one and only live terminal — because there is nowhere else to try it.
It recalculates the past
Not just from now on. It redraws roughly two weeks of history behind it.
The new values replace the old
Same bars, new numbers, written straight over the top of what was there.
Everyone's chart redraws
Quietly. Mid-session. With no notice and no record of what it used to show.
Nothing goes offline. Nothing errors. That is exactly the problem.
This is not a downtime problem — the service never becomes unavailable. It is change without warning, without a record of what the numbers were, and with no way to undo it except to tune again and hope.
~3,000
bars rewritten by one setting change
~2.2 weeks
of price history quietly redrawn
Zero
record of what the old values were
Notes: Be precise here: there is no outage today. The problem is mutation without provenance or control. A design that only prevented downtime would solve a problem this system does not have.

## Slide 5
STEP 3 — THE FIX
The fix, in one picture
TERMINAL A
live right now
TERMINAL B
rehearsing
its own
handover folder
its own
handover folder
✕
read
not read
THE READER
reads one folder,
and only one
Database
What you
and users see
To promote: move that arrow to the other folder.
One line of configuration, then restart the reader — seconds. Same database, same everything downstream. No new software, no changes to how data is stored, nothing for users to do.
Notes: The switch is a single argument on the collector service: which export directory it reads. Both terminals run and export continuously; only one folder is read. Promotion is that one argument plus a service restart.

## Slide 6
HOW IT RUNS, DAY TO DAY
The cycle — and the one rule that keeps it safe
1
A is live, B rehearses
B runs alongside with charts attached, producing output that nobody reads.
2
Tune B and look at it
Change settings, set the anchors, judge it by eye on B's own charts in MetaTrader.
3
Promote B
One switch. B goes live. A keeps running untouched, still holding the old settings.
4
Confirm, then swap roles
Once B is proven good in production, A is released and becomes the next rehearsal room.
and repeat, indefinitely
The one rule
Do not start tuning the terminal you just demoted until the newly promoted one is confirmed good. In that window it is the only undo that exists — and the moment you start changing it, you no longer have one.
Notes: The standby discipline rule from section 5.5. Between a promote and its confirmation, the demoted terminal is the only rollback path that exists.

## Slide 7
THE FINDING THAT CHANGES WHAT WE BUILD
One folder feeds four systems, not one
THE HANDOVER
FOLDER
one shared folder
Price and charts
What users actually look at.
moves with the switch
Fit-quality statistics
How well each setting is fitting.
moves with the switch
Economic calendar
The news-event feed.
would stop — with no error anywhere
Currency and gold strength
The separate index engine.
would stop later, just as quietly
Both failures
are silent
Neither one raises an alarm. A missing calendar file is read as "nothing to add today", by design — so the feed simply stops.
You'd notice days later, with nothing pointing back to the switch.
Notes: Lead with this slide. It is the single most consequential finding and is not visible from the existing topology diagram. Four independent lanes read the same export directory; a naive switch silently kills two of them.

## Slide 8
WHAT THAT MEANS FOR THE BUILD
So we build three terminals, not two
A
Rehearsal room 1
Carries the 26 tunable chart attachments, plus the news-event exporter.
TAKES ITS TURN BEING LIVE
B
Rehearsal room 2
Identical to A in every way — the same 26 attachments and the same exporter.
TAKES ITS TURN BEING LIVE
S
The steady one
Carries only the 8 currency and gold price feeds. Nothing on it has settings to tune.
NEVER SWAPS. EVER.
The news-event feed rides along harmlessly
It sits on both A and B. It has no settings to tune, so both produce identical output — whichever one is live makes no difference.
The index engine is simply pointed at S, permanently
It already reads its own separate setting on its own separate service, so this costs nothing to arrange and no code changes at all.
Cost: one extra terminal, roughly 300–500 MB of memory. Benefit: the two feeds that must not be disturbed become structurally impossible to disturb.
Notes: Option B from section 3.3. Only the genuinely tunable surface alternates. The calendar exporter and the OHLCV exporters are parameterless dumpers, so alternating them would buy nothing.

## Slide 9
THE ONE NEW RISK THIS DESIGN CREATES
Promoting a terminal that wasn't actually running
What would happen
Every one of its files is equally out of date.
They agree with each other perfectly — so every check passes.
The system reports itself completely healthy.
The newest bar simply stops moving forward.
Alerts keep running against a frozen price. It looks like a quiet market.
The fix: one extra question
WHAT WE ASK TODAY
“Do all the files agree with each other?”
WHAT WE ADD
“And is the newest bar actually recent?”
If not, reject the batch and log it — exactly like every other rejection we already handle.
One comparison. No new software, no database changes, nothing else touched.
Suggested threshold: twice the bar length — 10 minutes on the 5-minute chart, 30 minutes on the 15-minute. A wrong rejection fixes itself on the next pass a few minutes later; a missed one stays silent for days. So we err on the tight side deliberately.
Notes: Section 4. The completeness check is relative, not absolute — it verifies the sources agree with each other but never against the wall clock. A uniformly stale standby therefore validates clean. Threshold recommendation: 2 x TF_SECONDS, with the 105-second M5 margin explicitly accepted.

## Slide 10
WHAT PEOPLE ACTUALLY EXPERIENCE
What a switch looks like from the outside
0:00
The switch
A service restart — seconds. Nothing goes offline, nobody is logged out.
0:30 – 5:00
The repaint
The chart refreshes oldest bars first, working steadily toward the right-hand edge.
~6:00
Fully updated
Everything now reflects the new settings. Nothing was ever blank or broken.
No outage
at any point in the switch
~6,000
rows refreshed behind the scenes
5–6 min
until everything has caught up
And the undo? The old terminal is still running with its old settings — switch back and it takes over immediately. But be clear what that is: another forward switch, not a restore. The intermediate values are gone. The undo lives in the terminal, not in the data.
Notes: Section 5.3 and 5.4. Row selection is oldest-first, so the chart repaints left to right and the newest bars change last. Be honest about rollback: it reverses the effect but does not restore the previous data.

## Slide 11
AN HONEST SCORECARD
What this fixes — and what it doesn't
What it gives us
✓
Try a setting against the live market
without imposing it on anyone first.
✓
A single-action switch, no outage
no new software, no changes to how data is stored.
✓
The previous terminal stands ready
as a genuine, immediate way back.
✓
An honest forward test
every bar the candidate produces is data it has never seen — which is exactly the validation we've been unable to do.
What it still doesn't solve
–
No record of the old numbers
promoting still writes over shared history. Recovering what a chart showed last week would need a real change to how data is stored.
–
No automatic search
this proves one candidate a person assembled by hand — it can't sweep hundreds.
–
Slow, and one at a time
judging a candidate on live data costs real calendar days.
–
It won't notice drift for you
a person still has to spot that a setting has gone stale.
The limits matter as much as the capability — this is a physical, slow, but honest substitute for validation we currently cannot do at all.
Notes: Section 7. Do not oversell. The gain worth emphasising is that a candidate running live on a standby is immune to both blockers on walk-forward validation — MT5 computes it directly, and every bar arrives genuinely out-of-sample.

## Slide 12
THE PLAN FROM HERE
What happens next
1
Add the freshness check, with tests
Developer
Can start now
2
Write down the switch procedure
Developer
Can start now
3
Build terminals A, B and S
You, on the server console
Can't be done for you
4
Rehearse the first switch at a market close
You
After the terminals exist
ONE DECISION
TO CONFIRM
How old is “too old”?
Recommended: twice the bar length — 10 minutes on the 5-minute chart, 30 on the 15-minute.
Simple to reason about, and it catches a dead terminal within about ten minutes of a switch.
Steps 1 and 2 can start immediately and don't depend on the terminals existing. A real switch can't be verified until step 3 is done — so rehearse the first one at a market close, with the way back confirmed before it's ever needed in anger.
Notes: Build order from section 8. Items 1 and 2 are dev-verifiable and independent. Items 3 and 4 need VPS console access. Caution for the build: do not re-run install_services.bat to apply the service changes — set the individual service properties directly, or the live credentials get overwritten with placeholders.