## Slide 1
EXECUTIVE ARCHITECTURE SUMMARY
Part 06 + Part 07
Real-Time Market Data Pipeline
How price data travels from MetaTrader 5 terminals through the Flask MT5 service and the Next.js tier-access API to live candlestick charts in the browser.
Flask MT5 Service
Socket.IO WebSocket
Tier Access Control
Live Charting
Trading Alerts SaaS | Backend & API Architecture Deck

## Slide 2
Executive Summary
Combined scope of Part 06 (Flask MT5 Service) and Part 07 (Tier Routes API)
Part 06 is a standalone Flask microservice that connects to MetaTrader 5 terminals, resolves broker-specific symbols, and streams OHLCV candle data to the browser in real time over a Socket.IO WebSocket. Part 07 is a lean set of three Next.js API routes that enforce FREE/PRO tier entitlements — which symbols, timeframes, and combinations a user is allowed to request — before the frontend ever opens that WebSocket connection. Together they form a two-stage pipeline: authorize, then stream.
v2.0.0 architectural shift (2026-03-05)
Chart data delivery moved from HTTP polling to a persistent Socket.IO WebSocket. Part 07 no longer talks to MT5 directly — its only job now is tier authorization; all custom-indicator endpoints were removed in favor of OHLCV-only streaming.
29
Files in Part 06
Flask MT5 Service
3
Files in Part 07
Tier Routes API
0.25s
WebSocket change-
detection interval
2
Access tiers
FREE / PRO

## Slide 3
Technology Stack Overview
Libraries and frameworks powering each layer of the combined pipeline
Part 06 — Flask MT5 Service
Flask 3.0 + Flask-CORS 4.0 (REST layer)
flask-socketio 5.3 / python-socketio 5.10 / python-engineio 4.8
eventlet 0.33 (async workers, no Redis needed)
MetaTrader5 Python API — copy_rates_from_pos()
pandas / numpy (OHLCV processing)
psycopg2-binary 2.9 (PostgreSQL access)
pydantic ≥ 2.12 (response validation)
gunicorn 21.2 + gevent 23.9 (production server)
pytest / pytest-flask (test suite)
Part 07 — Tier Routes API
Next.js 15 App Router API routes (TypeScript)
GET /api/tier/symbols — accessible symbols by tier
GET /api/tier/check/[symbol] — single-symbol access check
GET /api/tier/combinations — valid symbol+timeframe pairs
lib/tier-config.ts + lib/tier-validation.ts (shared logic)
zod schema validation
Session-based authentication guard on every route
No MT5 or indicator logic (removed in v2.0.0)
Frontend Consumption
React 19 + Next.js 15 client components
socket.io-client 4.8 (WebSocket connection)
lightweight-charts 5.2 (candlestick rendering)
hooks/use-ohlcv-socket.ts (subscribe / stream hook)
trading-chart-client.tsx + trading-chart.tsx
HTTP polling removed — WebSocket-only updates
@socket.io/redis-adapter (multi-instance scaling, backend)

## Slide 4
System Architecture
How Part 06 and Part 07 fit together with the browser and MT5 terminals
Browser
React + lightweight-charts
socket.io-client
Part 07
Tier Routes API
Next.js API routes
FREE/PRO authorization
Part 06
Flask MT5 Service
flask-socketio + eventlet
Symbol resolver, tier check
MT5 Terminals
MetaTrader5 Python API
15 symbols / 15 terminals
1. Authorize first: Browser calls Part 07 (GET /api/tier/combinations) to fetch which symbol + timeframe pairs the user's tier allows.
2. Stream second: Browser opens a Socket.IO connection directly to Part 06, which re-validates tier access before subscribing the room.
3. Source of truth: Part 06 polls MT5 terminals every 0.25s and pushes only on new bars or intra-bar price changes — idle chart tabs cost zero resources.

## Slide 5
Data Flow, Step by Step
From page load to a live-updating candlestick on screen
1
Fetch allowed combinations
Part 07
Chart page calls GET /api/tier/combinations — Part 07 returns the symbol + timeframe pairs the signed-in user's tier permits.
2
User selects symbol + timeframe
Frontend
Dropdowns are populated only with tier-eligible choices; invalid combinations are blocked client-side.
3
Open Socket.IO subscription
Part 06
Browser emits subscribe {symbol, timeframe} to the Flask service; tier access is re-checked server-side before joining the room.
4
Receive initial_data
Part 06
Flask reads OHLCV history via MT5's copy_rates_from_pos(), resolves the broker symbol name, and emits the full candle history once.
5
Stream ohlcv_update events
Part 06
A background loop checks each active room every 0.25s and pushes only when a new bar opens or the current bar's close price changes.
6
Render live candles
Frontend
trading-chart.tsx renders updates via lightweight-charts — no HTTP polling; idle tabs consume no backend resources.

## Slide 6
Key Design Decisions
Notable choices behind the current architecture
WebSocket over polling
Chart data delivery migrated from HTTP polling (trading-chart.tsx) to a persistent Socket.IO stream. Both FREE and PRO users get real-time pushes; tier limits control which symbols/timeframes, not the delivery speed.
Tier enforcement stays server-side
Part 07 gates which combinations the UI can request; Part 06 independently re-validates tier access before opening a Socket.IO room — access control is never trusted to the client.
No custom indicators by design
MT5 Python API's iCustom() and copy_buffer() proved unreliable for fractals/trendlines. Part 06 now serves OHLCV only; all indicator values come from Part 20 (SQLite-Sync), fed by MQL5 expert-advisor exports.
Efficient by default
The 0.25s loop is a change-detection interval, not a fixed broadcast rate — it pushes only on new bars or close-price ticks. Subscription rooms exist only while a browser tab is open on that chart, so idle symbols cost nothing.